## Slide 1: The Laser-hybrid Accelerator for Radiobiological Applications LhARA

## Slide 2: Plan
Challenges and opportunities
Radiobiology
LhARA
New techniques with wide application
Conclusions

## Slide 3: Challenges and opportunities
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 4: Radiotherapy; the challenge
Cancer: second most common cause of death globally
  Radiotherapy indicated in half of all cancer patients
Significant growth in global demand anticipated:
  14.1 million new cases in 2012 ⇢ 24.6 million by 2030
  8.2 million cancer deaths in 2012 ⇢ 13.0 million by 2030
Scale-up in provision essential:
  Projections above based on reported cases (i.e. high-income countries)
  Opportunity: save 26.9 million lives in low/middle income countries by 2035
Provision on this scale requires:
  Development of new and novel techniques … integrated in a
  Cost-effective system to allow a distributed network of RT facilities
Atun, Lancet Oncol. 2015 Sep;16(10):1153-86

## Slide 5: The benefit of particles
Maximise therapeutic benefit by:
  Maximising damage to tumour
  Minimising damage to healthy tissue
X-ray therapy:
  Modality used in most radiotherapy
  Dose falls exponentially with depth
  Proximity of sensitive organs limits dose to tumour

## Slide 6: Particle-beam therapy
Proton and ion-beam therapy:
  Bulk of dose deposited in Bragg peak
  Significant normal-tissue sparing (entry)
  Almost no dose beyond the Bragg peak

## Slide 7: The need for a step-change in capability
Growing recognition of benefits of PBT worldwide:
  70 PBT centres in operation; 40 under construction
‘Incremental’ development of technique
  Existing suppliers
  New initiatives
Exciting indications of benefits of novel beams …

## Slide 8: Particle beam therapy today
Cyclotron based:
  Limitations:
    Energy modulation
    Instantaneous dose rate
Synchrotron based:
  Limitiations:
    Complexity
    Instantaneous dose rate
Christie Hospital Manchester
MedAustron Austria
 reduce footprint, cost and complexity
‘PBT for the many’!
 increase flexibility
optimize treatments

## Slide 9: Radiobiology
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 11: The case for fundamental radiobiology
Relative biological effectiveness:
  Defined relative to reference X-ray beam
  Known to depend on:
    Energy, ion species
    Dose & dose rate
    Tissue type
    Biological endpoint
Yet:
  p-treatment planning uses 1.1
  Effective values are used for C6+
Maximise the efficacy of PBT now & in the future:
  Require systematic programme to develop full understanding of radiobiology
Paganetti, van Luijk (2013)
SemRadOncol

## Slide 12: Biological impact from the physics of ionisation
Low-LET radiation:
  Repairable single/double strand breaks
High-LET radiation:
  Complex DNA lesions
    Multiple DNA pathways
    More difficult to repair
    Enhances cell death
Programmatic approach:
  Dynamic studies of impact of radiation
  Interpret with advanced computer models (e.g. G4DNA)

## Slide 13: A complex, multi-facetted problem
Time
Multidisciplinary approach essential
Carter et al, and Parsons (2018) IJROBP & (2019) IJROBP

## Slide 14: Radiobiology in new regimens
Worked example: FLASH
Conventional regime : ~2 Gy/min
FLASH regime : >40 Gy/s
Evidence of normal-tissue sparing while tumour-kill probability is maintained:
i.e. enhanced therapeutic window
Time line:
Initial reports: 2014 (e.g. Flauvadon et al, STM Jul 2014)
Confirmation in mini-pig & cat: 2018 (Clin. Cancer Research 2018)
First treatment 2019 (Bourhis et al, Rad.Onc. Oct 2019)

## Slide 15: Radiobiology in new regimens
Prezado; 13Nov19
Worked example: micro beams
Conventional regime : > 1 cm diameter; homogeous
Microbeam regime : < 1 mm diameter; no dose between ‘doselets’
Remarkable increase of normal rat brain resistance.
[Dilmanian et al. 2006, Prezado et al., Rad. Research 2015]
Dose escalation in the tumour possible – larger tumor control prob.

## Slide 16: Radiobiology in new regimens
The ideally flexible beam facility can deliver it all!
 substantial opportunity for a step-change in understanding!
Time
domain
Space
domain
Energy
Ion
species
In combination and with chemo/immuno Therapies

## Slide 17: Laser-hybrid Accelerator for Radiobiological Applications
LhARA; a novel, hybrid, approach:
  High-flux, laser-driven proton/ion source:
    Overcome instantaneous dose-rate limitation
    Delivers protons or ions in very short pulses:
      Pulse length 10 – 40 ns
    Can provide arbitrary pulse structure
  Novel plasma-lens capture & focusing
  Fast, fixed-field post acceleration
 compact, uniquely flexible facility
LhARA consortium

## Slide 18: Our vision and our ambition
LhARA will be a uniquely-flexible, novel system that will:
Deliver a systematic and definitive radiobiology programme
Prove the feasibility of the laser-driven hybrid-accelerator approach
Lay the technological foundations for the transformation of PBT
  automated, patient-specific: implies online imaging & fast feedback and control

## Slide 19: LhARA
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 20
LhARA

## Slide 21: LhARA; overview
Laser-driven source:
  Enormous instantaneous dose
    Overcome space-charge limit of today’s ion sources
Proton/ion capture using plasma (Gabor) lens:
  Electrostatic focusing, short focal length:
Post-acceleration using fixed-field accelerator:
  Rapid, energy-efficient acceleration of protons or ions
    Protons up to 127 MeV p;
    Ions up to ~35 MeV/u
Staged implementation:
  Stage 1: In vitro studies with protons at energies up to 15 MeV
  Stage 2: In vivo & in vitro studies with protons up to 127 MeV and ions up to 35 MeV/u

## Slide 22: Sheath acceleration
Laser incident on foil target:
  Drives electrons from material
  Creates enormous electric field
Field accelerates protons/ions
  Dependent on nature of target
First observation ~2000
Active development:
  Laser: power and rep. rate
  Target material, transport
Schwoerer, H. et al., 2006; Nature, 439(7075).

## Slide 23: Laser-driven proton/ion source
Advantage:
  Enormous proton/ion flux at 10—15MeV in tiny (30 fs) pulse at 10 Hz
Issue to be solved:
  Efficient capture, focusing, selectin and manipulation of divergent ion beam
Ti:Sapphire commercial system >15TW
Pulse ~35fs at rep-rate of at least 10Hz
At least 500mJ laser energy - IL ~ 1020 Wcm-2

## Slide 24: Beam capture/production principle
Plasma (Gabor) lens:
  Strong focusing exploiting electron plasma in solenoid
Posocco, Pozimski

## Slide 25: LhARA: ion-source development
Capture
Electron plasma:
  Strong focusing of +ve ions
1st prototype:
  1 MeV protons Surrey Ion Beam Centre
  Aberrations observed
Upgraded prototype:
  Under development Imperial
Laser source/capture test
Integration test:
  Gabor lens on cerberus Laser at Imperial
Plan:
  “Now”: prepare to validate lens with a
  Next: test using laser-driven source

## Slide 26: LhARA; stage 1
Pasternak
Capture @ 10—15 MeV
Energy selection
Phase-space matching
Vertical arc
11.6 m
Laser

## Slide 27: LhARA – Stage 2
In-vitro radiobiology using animal models:
  Post-acceleration required
Baseline:fixed field accelerator:
  x3 increase in momentum
    15 MeV protons accelerated to 127 MeV
    3.8 MeV/u carbon 6+ ions accelerated to 33 MeV/u

## Slide 28: Fixed Field Accelerator
Advantages over conventional medical cyclotron
  Variable energy operation without energy degraders
  Operation with different ions
  Multiple extraction ports
Bending magnetic fields do not vary in time.
  Rapid acceleration.
Alternating gradient gives strong focussing.
Very large acceptance.
  Useful, e.g. to accelerate muon beams.

## Slide 29: FFA potted history
Early 1950s, FFAG developed independently:
  Japan by Tihiro Ohkawa
  US by Keith Symon
  Russia by Andrei Kolomensky.
The first prototype was operated in 1956
  Jones, Terwilliger, Technical Report MURA-LWJ/KMT-5 (MURA-104), April 3, 1956.
Not much activity until first proton accelerator in 2000
PRISM muon beam phase rotation demonstration ring at Osaka.
The Michigan Mark I FFA 400KeV electron accelerator was the first operational FFA.
EMMA at Daresbury
500 keV Proton proof-of-principle FFA at KEK.
Kyoto University FFA for ADSR

## Slide 30: LhARA FFA
Parameters
Number of sectors 10
k 5.19
Spiral angle 47.64°
Rmax 3.49 m
Rmin 2.92 m
Bmax 1.4 T
Max Proton injection energy 15 MeV
Max Proton extraction energy 127.4 MeV
h 1
RF frequency
for acceleration (15-127.4MeV) 2.89 – 6.48 MHz
Bunch intensity ~108 protons
Pasternak

## Slide 31: Present multidisciplinary collaboration
Further interest from:
Groups in the UK and overseas
The International Biophysics Collaboration [spokespeople: Patera, Prezado]

## Slide 32: The next steps
Preparation of ‘pre-CDR’ for LhARA:
  Deliverable: pre-CDR for LhARA [milestone April 2020]
  Very modest resources
  Milestone set to allow next wave of bids
LhARA and radiobiology test facility:
  Deliverable: proton-FLASH dosimetry [milestone April 2020]
  Again, very modest resources
International Biophysics Collaboration (IBC):
  ‘Networking activity’ [milestone September 2021]

## Slide 33: New techniques with wide application
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 34
Higgs
Boson
Higgs
Boson
Generations of matter
III
II
I
Force Carriers
Z
Z boson
W
W boson
g
photon
g
gluon
t
tau
n
t
t-neutrino
b
bottom
t
top
m
muon
n
m
m-neutrino
s
strange
c
charm
e
electron
ne
e-neutrino
Leptons
d
down
up
u
Quarks
The Standard Model

## Slide 35: Energy frontier to illuminate limit of SM
Measurement at highest possible energy
  Experimental motivation clear!
    Theorists motivated by ‘meta-stability’ of SM
Hernandez, Granada, 2019
Degrassi et al, 10.1007/JHEP08(2012)098

## Slide 37
Neutron scattering facilities in Europe; Present status and future perspectives
ESFRI Physical Sciences and Engineering Strategy Working Group Neutron Landscape Group
STFC, Neutron scattering Materials research for modern life

## Slide 38: Options for ⎷s x 10
250—350 GeV for Higgs & e/w CepC, ILC &/or CLIC
pp @ 100 TeV
⎷s ⇢ 10 TeV for exploration FCC-hh

## Slide 39: Laser-driven acceleration
Shrink footprint using ultra-high gradient acceleration:
  Exploit plasma waves
/ particle
Excitation of plasma:
  Photon (laser)
  Particle beam:
    Electron or proton
P. Ratoff, CI/Lancaster

## Slide 40: High-power driver for neutron production
High power:
  Required to serve many beamlines
    Maximise scientific return
Example:
  ISIS II:
    Consider Fixed-Field Accelerator (FFA):
    Reduced power consumption
J. Thomason, G. Aymar:
[ISIS II] PROJECT LIFECYCLE PLAN

## Slide 41: Neutrinos from stored muons
Scientific objectives:
  %-level (νeN) cross sections
    Double differential
  Sterile neutrino search
    Beyond Fermilab SBN
  Muon-accelerator R&D
    FFA optics; cooling …
Precise neutrino flux:
  Normalisation: < 1%
  Energy (and flavour) precise
p ⇢ m injection pass:
  “Flash” of muon neutrinos

## Slide 42: Conclusions
The Laser-hybrid Accelerator for Radiobiological Applications (LhARA)

## Slide 43
2040
2050
1970
1980
1990
2000
2010
2020
2030
1946
↓
1960
Novel accelerator techniques
System: image processing
fast feedback, control
Fundamental
radiobiology

## Slide 44
Novel accelerator techniques
System: image processing
fast feedback, control
Fundamental
radiobiology

## Slide 45: Conclusions
Laser-hybrid approach has potential to:
  Overcome dose-rate limitations of present PBT sources;
  Deliver uniquely flexible facility:
    Range of ion species, energy, dose, dose-rate
  Disruptive/transformative approach ‘for 2050’ …
Opportunity:
  Develop and prove novel systems in production system;
  Deliver research facility dedicated to radiobiology;
  Contribute to study of biophysics of charged-particle beams
First and next steps:
  Initial concept developed and prototype evaluation underway
  Working towards ‘pre-CDR’ for LhARA
  Wonderful opportunity to build novel techniques to spin back in!