## Slide 1
Yolanda Prezado
New approaches in radiation
therapy

## Slide 2: Radiotherapy (RT)
Medical use of ionizing radiation for treatment of cancer and some other types of benign lesions, like arterious-venous malformations.
Example of a rapid technological transfer
  1895: Roentgen discovers X-rays
  1895: First RT treatment (recurrent breast cancer,
  Grubbe, Chicago)
  1896: Stomach cancer treatment (Freund, Viena).
At least 50 % of all cancer patients will receive radiotherapy at some stage during the course of their illness (Delanay et al., 2005).

## Slide 3: Radiotherapy types

## Slide 4: External radiotherapy
Medical lineal accelerators (RF)
Mainly 6 and 18 MV photons.
“Large field sizes” (several squared cm)
& homogenous dose distributions
Temporal fractionation of the dose
Dose rates around 2 Gy/min
2 Gy/session, 1 session/day,
5 sessions per week, 5-6 weeks
Notes: Algun video?

## Slide 5: New approaches in Radiotherapy: why?
Radiotherapy is one of the most important methods for cancer treatment.
Remarkable technical advancements BUT the same few temporal and spatial dose distributions
Main limitation in radiotherapy : normal tissue tolerances
Unsatisfactory treatment of radioresistant tumors (i.e. gliomas)
& pediatric cancers
Physics
Biology
Medicine

## Slide 6
Rethink radiation therapy

## Slide 7
Space
Time
Energy/particle
Standard RT
Using physics to modulate the biological response
Homogeneous dose distributions
Large field sizes
Mostly photons
Time fractionaction: 2 Gy/fraction,
1 fraction/day, 30-35 fractions

## Slide 8
Space
Energy/particle
Standard RT
Using physics to modulate the biological response
Time

## Slide 9: Temporal fractionation of the dose
– Reoxygenation
– Reassortment
Tumor control
Normal tissue preservation
– Repair of sublethal damage
– Repopulation of cells
Common scheme: 2 Gy/session, 1 session/day, 5 days week, 5-6 weeks

## Slide 10: Temporal fractionation of the dose
Other schemes being explored
Hypofractionation (higher doses-less days)
benefit for some prostate, breast, lung cancers
Hyperfractionation (lower doses, twice per day, more days)
advantageous for some head-and-neck and cervical squamous cell cancers
Continuous hyperfractionated accelerated radiation therapy (three small sessions per day) used to treat lung cancer
TIME MATTERS

## Slide 11: High single dose can estimulate immune system
High single dose radiation (30 Gy) increases CD8+ T cells in the stroma of tumors with induced remissions
Baker et al, Clin. Cancer research 2015
BALB/c mice. CT26 & MC38 colon tumors

## Slide 12: Dose rate
In general dose rate cells killing (time to repair)
However, in some cases of low dose rates inverse dose rate effect.
No systematic evaluations performed at very high dose rates.
Notes: MEJORARLAAA

## Slide 13: Time: Dose rate
FLASH irradiation the dose is given at ultrahigh dose rate (> 40 Gy/s)
Differential effect tumor-healthy tissues
    Equivalent tumor control to standard RT
    Significantly reduces side effects in
    normal tissues.
    The advantage of Flash radiotherapy confirmed in mini-pig
    and cat-cancer patients. Clin. Cancer Research 2018.
    Main challenge: dosimetry with ultrahigh dose rate
Favaudon et al. 2014

## Slide 14
Space
Energy/particle
Standard RT
Using physics to modulate the biological response
Time

## Slide 15: Addressing a clinical need with a new paradigm
Standard radiotherapy
< 1 mm
1-2 mm
+
Large beam sizes (> 1 cm2)
Homogeneous
dose distributions
Spatial fractionated radiotherapy
x-rays minibeam radiation therapy
Narrow beam sizes spaced by areas of low dose
+
Heterogeneous distributions
> 1 cm

## Slide 16: Addressing a clinical need with a new RT paradigm
> 1 cm
+
Remarkable increase of normal rat brain resistance.
Dilmanian et al. 2006, Prezado et al., Rad. Research 2015
Dose escalation in the tumor possible higher tumor control
Distinct biological mechanisms not yet understood
Standard RT
Spatial fractionated radiotherapy
x-rays minibeams radiation therapy
Large beam sizes (> 1 cm2)
Homogeneous
dose distributions
< 1 mm
1-2 mm

## Slide 17
The GRID approach
1909 Alban Köhler used a “perforated screen” in orthovoltage machines Skin toxicity reduction
GRID therapy with megavoltage radiation beams (LINACS)
Meigooni et al, Med. Phys. 2006
Mainly for palliative treatment of bulky, massive tumors
Beam widths ≥ 1 cm2
Single fraction 15-20 Gy
TNF-α induction (Sathishkumar et al, 2002)

## Slide 18
LINAC-based GRID therapy: “limits”
-Relative small output
Beam sizes > 1 cm2
-Important scattering of MV beams 
Small peak-to-valley dose ratio: 2 to 5
(high PVDR favor tissue sparing)
The GRID approach

## Slide 19
Moving forward

## Slide 20
Moving forward

## Slide 21
Playing with the beam size
Dose-volume effect: the smaller the field size is, the higher the tolerance
Zeman et al., Science (1959)

## Slide 22
European synchrotron radiation facility
~ 300 m
The medical beamline ID17
White beam dose rate 10000 Gy/s
Negligible divergence
Low Energy X-rays
Synchrotron micro and minibeam radiation therapy

## Slide 23: Microbeam Radiation therapy
MRT uses 50 µm-wide beams, spaced by 400 µm
Slatkin et al. Med. Phys. 1992
Differential effect normal tissue versus tumor observed in animal experiments
Normal (brain) is able to withstand
more than 300 Gy/one fraction
Laissue et al, SPIE 2001
Tumor control effectiveness in glioma-bearing rodents
Laissue et al, Int.J. Cancer 1998
600 Gy

## Slide 24: Drawbacks of MRT
Requires extremely high dose rates
Scarce beamtime at synchrotrons
Difficult realization of clinical trials
Not favourable dosimetry (low-energy X-rays)
High doses to control tumors 300-600 Gy.
Good compromise: Minibeam radiation therapy
Dilmanian et al., PNAS 2006

## Slide 25: Minibeam radiation therapy: a good compromise
25
Beam widths: 500-700 µm  transfer to low cost equipment possible
Prezado & Dos Santos et al. Scie. Reports 2017
25
Gain in normal tissue tolerances
Whole rat brain irradiation (20 Gy average)
Tumor control effectiveness
F98 glioma-bearing rats
Proof of concept

## Slide 26
Moving forward… Proton minibeam radiation therapy (PROTONMBRT)

## Slide 27: PROTONMBRT: an innovative therapeutic approach
Protons and their specific physics and biology
Minibeam radiation therapy
Proton minibeam radiation therapy
Prezado et al. Med. Phys.2013
Tumor
First implementation worldwide at a Orsay proton therapy centre (I. Curie)
(Peucelle, Martinez,… and Prezado, Med. Phys. 2015)

## Slide 28
PROTONMBRT
Proof of concept

## Slide 29
First evaluation of normal brain response (Prezado et al. Scie. Rep. 2017)
Standard PT (25 Gy/one fraction)
pMBRT (25 Gy average dose-
58 Gy peak dose/one fraction)
Skin: moist desquamation
Permanent epilation
Important brain damage
No skin damage
Reversible epilation
No brain damage observed
No cognitive effects observed
Proton minibeam radiation therapy spares normal brain
Whole brain irradiations (normal rats, 7-weeks old). Long-term follow up (6 m)
VERSUS
NET REDUCTION IN NEUROTOXICITY

## Slide 30: Tumor control effectiveness in glioma (RG2) bearing rats
25 Gy/one fraction
pMBRT  67 % of long-term survivals (free of tumor).
Among the best results ever obtained with radiotherapy alone
Prezado et al., Red Journal 2019
Standard PT
pMBRT
Tumor
Tumor

## Slide 31: pMBRT provides tumor control even with highly heterogeneous dose distributions
INHOMOGENOUS dose distribution
70 Gy in the peak  30 Gy average
Whole brain irradiation, 8 days after implantation (n=10)
Without significant toxicity
Prezado et al. Scie. Reports 2018

## Slide 32
Proton minibeam radiation therapy widens the therapeutic window for gliomas

## Slide 33: Short term objectives (3-5 years)
To reach Phase I/II clinical trials
PROTONMBRT
Proof of concept in
small animals
Clinical trials
ERC consolidator grant (2019-2024)
Generation of intense minibeams at a clinical center
Challenging dosimetry (extremely small field sizes)
Radiobiology
  -To find the physical parameters maximizing the therapeutic index
  -To unravel the biological mechanisms

## Slide 34: PROTONMBRT
The increase of the tolerance doses of normal tissue by pMBRT offers
  Potential benefit for paediatric oncology  Reduced risk of complications
  Allows dose escalation  Efficient treatment of radioresistant tumors
  Cost reduction:
  -pMBRT enables hypofractionation schemes
  -Reduced requirements of targeting
  Reflection on first I clinical trials
A novel radiotherapy concept to solve an urgent medical need

## Slide 35
Moving forward… Heavy ions minibeam radiation therapy

## Slide 36: Heavy ions MBRT: Advantages
Reduced MSC high PVDR in normal tissue
Narrow beams possible (500 µm)
Gonzalez, Peucelle and Prezado, Med. Phys 2017
Possible synergies of MBRT effects with the higher capacity of ions to inhibit angiogenesis and activate immune system

## Slide 37: Heavy ions MBRT: impact on valleys
Large beam spacing (ctc) minimize
the contribution of high LET fragments to the valleys
Heavier fragments
are dominant in the valleys at the target position, which might favor tumor control.
Gonzalez, Peucelle and Prezado, Med. Phys 2017
Larger Beam spacing
Tumor
Tumor

## Slide 38: Heavy ions MBRT: disentangling molecular and cellular effects with infrared microspectroscopy
I. Martinez et al., in preparation
U87 cells irradiated with Carbon MBRT or conventional broad beams @ HIT

## Slide 39: Very heavy ions MBRT
Ne, Si and Ar ions used in the past, extremely efficient for the treatment of hypoxic tumors (Castro 1994)
HOWEVER, abandoned due to important side effects in normal tissues
Very heavy ions (low OER) + MBRT (sparing of normal tissue)
Improvement of therapeutic index
Peucelle, Martinez and Prezado, Med. Phys. 2015
Our hypothesis

## Slide 40: Ne ions MBRT at HIMAC (Japan)
BJ human foreskin fibroblasts irradiated with
230 MeV/A Ne ions
First in vivo experiment planned January 2020
First results indicate higher DNA damage in standard RT (infrared spectroscopy)
Different cytokine expression (ongoing analysis)
Notes: Exper HIMAC

## Slide 41
Space
Energy/particle
Standard RT
Using physics to modulate the biological response
Time

## Slide 42: Very high energy electrons (VHEE) therapy
VHEE therapy (70-250MeV) is considered as a potential cost-effective approach to improve cancer treatments.
Collaboration with Laser-LOA
VHEE grid therapy approach
Martinez, Fois and Prezado, Med. Phys. 2015

## Slide 44: Dose rate effects: FLASH
Impact of different beam structure and energy on FLASH effect:
0
300 MeV
7 MeV
70 MeV
Oriatron-
Inst. Curie
Laser-LOA
µs
fs
Bunch width
Repetition rate

## Slide 45: Final reflections
The dose delivery method may have an important impact on biological response.
Not need to deposit a lethal dose in each of the tumor cells to kill it.
Non-targeted effects can play a major role in RT treatments
Charged particles (p, heavy ions) allow to fully profit from the advantages of spatially fractionated radiotherapy

## Slide 46: International Biophysics collaboration
Why?
  New accelerators under construction worldwide, very expensive facilities who plan biomedical research.
  Important to coordinate the efforts to avoid duplications and instead have synergistic interactions for biomedical research
New beams: higher energy, higher intensity, different beam structure

## Slide 47: Frontiers in Physics: research topic issue
Recruiting papers

## Slide 48: NARA team
C. Guardiola
C. Lamirault
R. Delorme
T. Schneider
I. Martinez
M. Dos Santos
J. Bergs
C. Peucelle
W. Gonzalez
Acknowledgments
Biology Service of IMNC: M. Juchaux

## Slide 49: Acknowledgments
IR4M
C. Sebrie
Experimental RT
platform
F. Pouzoulet
D. Labiod
C. Roulin
Orsay Proton
therapy Center
A.Patriarca
L. De Marzi
C. Nauraye
R. Dendale
E. Hierso
Institut Pasteur
G. Jouvion
D. Hardy
Institut Curie

## Slide 50
Thank you very much for your attention!
yolanda.prezado@curie.fr