## Slide 1: Accelerator challenges for the CERN Next Ion Medical Machine Study (NIMMS)
Elena Benedetto, SEEIIST Association
8th June 2022, CCAP Seminar – Imperial College
Special acknowldgement:

## Slide 2: Proton (ion) radiation therapy
DOI:10.1016/j.ijrobp.2016.06.2446
Bragg Peak: charged particles deposit energy @ specific depth, depending on the beam energy
110 particle - proton therapy facilities,
30 in Europe (Vs. 14’000 X-ray facilities)
photons IMRT
protons
HITACHI Synchrotron
IBA SynchroCyclotron
3D beam scanning

## Slide 3: Carbon (and other) ions therapy
Range 3 mm to 300 mm in water-equivalent (Bragg Peak)
Protons: 60 - 250 MeV (Br = 2.42 Tm )
Carbon: 100 – 430 MeV/u (Br = 6.6 Tm)
X-ray
Proton
Carbon
Marx, Nature, 2014
Single-strand breaks (easy to repair) vs. double-strand breaks (not reparable)
3x more damage (RBE)
also in oxygen-depleted “radioresistant” tumours
~2.7x beam rigidity, i.e. more difficult to bend
MedAustron, 25 m diameter synchrotron, 3 treatment rooms, no C-ion gantry
HIT C-ion gantry (600 tons)
Facility becomes larger and more expensive
~200 MEur
Helium and Oxygen ions also of interest for treatment

## Slide 4: Carbon ion synchrotrons – new developments
Superconducting (SC) magnets to reduce dimensions, weight (and cost) of the facility
  compact synchrotron and gantry
Higher (x10) beam intensity stored:
  to deliver full beam in one cycle and overcome limitation of long SC magnet ramping rates
  to be ready for FLASH treatment modalities
I’ll talk about:
  What is NIMMS, SEEIIST, HITRIplus
  New developments and studies @ NIMMS

## Slide 5: The CERN Next Ion Medical Machine Study (NIMMS) leverages on CERN expertise to develop a portfolio of technologies (…a “toolbox”) for a new generation of medical accelerators with ion beams
PIMMS in 2000 gave birth to CNAO/MedAustron
NIMMS launched (funded) as a Knowledge Transfer initiative in 2019.
Open to collaborations internal and worldwide:
  SEEIIST, TERA Foundation, GSI, INFN, Imperial College, U. Manchester, Cockcroft Institute, U. Melbourne, CIEMAT, CNAO, MedAustron, Riga University, DKFZ, U.Thessaloniki,…
Support from EU programs: HITRIplus and iFAST.
Input from medical/scientific community via ENLIGHT and the International Biophysics Collaboration.
Bi-weekly (Friday) seminars attended by ~30 participants
HF Linac
Gantry
Synchrotron
Magnets
AI/ML*
R-isotopes*
* in preparation
https://indico.cern.ch/event/956260/
(M. Vretenar KT seminar Oct’20)

## Slide 6: NIMMS - Specifications from the scientific community
Delivery
Using multiple ions (Carbon, Helium and others);
Fast dose delivery;
Equipped with a SC gantry;
With range calibration and diagnostics online.
Accelerator
Higher beam intensities than present in EU (~1010 C-ions);
Reduced footprint, to about 1’000 m2;
Lower cost, compared to present (~120 M€);
Lower running costs.
Archamps Workshop, June 2018

## Slide 7: SEEIIST as strategic partner and reference user
SEEIIST: South East Europe International Institute for Sustainable Technologies
Consortium of 10 countries, to construct a facility for cancer Research & Therapy in South East Europe.
Science for Peace: to build international cooperation and scientific capacity.
Initiated in 2017 by H. Schopper, former DG of CERN, and S. Damjanovic, physicist and (ex) Minister of Science.
2008 Yellow Book, by U. Amaldi et al.
Accelerator design studies started in 2019 at CERN, supported by EU and continue now within HITRIplus (Apr’2021), in tight collaboration with CERN and EU partners.
Science for peace
Scientific excellence
Education & Training
Green infrastructure

## Slide 8: SEEIIST advanced accelerator
Research and therapy with ions: p, He, C, O,…up to Ar
Flexible extraction modality (multi-energy slow resonant extraction and FLASH)
Intensity x20(*) European facilities
Baseline layout is a NC-magnet synchrotron (like CNAO/MedAustron)
Option of a compact SC-magnet synchrotron
 | p | He | C
Intensity | 2.6 e11 | 8.2 e10 | 2.0 e10
Injection Energy (MeV/u) | 7-10 | 5 | 5
Extract Energy (MeV/u) | 60-250 | 60-250 | 100-430
Beam rigidity max (Tm) | 2.42 | 4.85 | 6.62
Synchrotron diameter (m) | ~25m |  | 
Spill duration (s) | 0.1 - 60 |  | 
Spill ripple @1 kHz (Imax/Iave) | <1.5 |  | 
(*)To deliver 2 Gy to 1 liter in one cycle
Technologies e.g. advanced injection/extraction are developed for both normal conducting (NC) and super conducting (SC) -magnet synchrotrons.

## Slide 9: HITRIplus
Courtesy S. Rossi
Starting Community Integrating Activity of the Horizon 2020 EC Framework Programme covering 04/2021-03/2025,
5 M€ total EC contribution, 1.2 M€ for accelerator studies to SEEIIST, CERN, Bevatech, CNAO, MedA, INFN, CEA, CIEMAT, PSI, UU, Wigner

## Slide 10: HITRIplus structure
8/6/2022 – CCAP Seminar Imperial College

## Slide 11: NIMMS: three synchrotrons designs for medical ions
SEEIIST layout, https://cds.cern.ch/record/2748083
https://arxiv.org/abs/2105.04205
E. Benedetto, U. Amaldi et al. @ TERA
  Helium-only, warm
  Compact (C=27m), with SC-magnets AG-CCT
  PIMMS-lattice (C=75m), intensity x20 (SEEIIST baseline)
M. Vretenar et al., IPAC22
 | p | He | C
Intensity* | 2.6 e11 | 8.2 e10 | 2.0 e10
Inj. E (MeV/u) | 7-10 | 5 | 5
Extr. E (MeV/u) | 60-250 | 60-250 | 100-430
Br max (Tm) | 2.42 | 4.85 | 6.62
Spill ripple Imax/Iave @1 kHz | <1.5 |  | 
Spill duration (s) | 0.1 - 60 |  | 
*To deliver 2 Gy to a 10x10x10 cm3 in one cycle

## Slide 12: 1) SEEIIST baseline
SEEIIST layout, https://cds.cern.ch/record/2748083
  PIMMS-lattice (C=75m), intensity x20 (SEEIIST baseline)
Collaboration w. U. Melbourne
Research and treatment:
50% day-time devoted to research: radio-biology, veterinary, material science, …
Separation between clinical and experimental area
Experimental area is modular
Linac and sources separated from synchrotron
Potentially expanded to for radio-isotope production (from linac)
X. Zhang, alternative lattice based on DBA

## Slide 13: 2) SC-magnets compact ring for C-ions
Evolved to triangular, to “ease” magnets design
@TERA
https://arxiv.org/abs/2105.04205
Optics is preliminar, inj/ext to be designed yet
Based on 3.5T 60 deg AG-CCT

## Slide 14: Strongly curved CCT magnets challenges
Parameter | Synchrotron magnet | Prototype Magnet
B (Tm) | 6.6 | 6.6
B0 dipole (T) | 3.0 | 4-5
Coil apert. (mm) | 70-90 | 60 (90)
Curvature radius (m) | 2.2 | 2.2 , 
Ramp Rate (T/s) | 1 | 0.15-1
Field Quality (10-4) | 1-2 | 10-20
Deflecting angle | 90 | 0 - 45
Alternating-Gradient | yes (triplet) | N/A
Quad gradient (T/m) | 40 | 40
Bquad peak (T) | 1.54- 1.98 | 1.2
Bpeak coil (T) | 4.6 - 5 | 5.6-7
Operating current (kA) | < 6 | < 5
Type of Superconductor | NbTi (Nb3Sn) | NbTi (curved), HTS (straight)
Operating temperature (K) | 5 (8) | 5 (20)
Magnet Parameters for HITRIplus
Lucio Rossi
Collaboration w. INFN, partners in HITRIplus and iFAST and U.Manchester

## Slide 15: Field Quality for curved magnets 1/3
Vs.
Multipole expansion, FFT on a reference radius
Rotating coil method
Only in straight geometry the coefficients are the same…
We define FQ using field derivatives, not multipoles
EB and D. Barna, WG – field quality
Collaboration w. INFN, partners in HITRIplus and iFAST, U.Manchester, CERN ABP

## Slide 16: Field Quality for curved magnets 2/3
D. Veres, D. Barna
In straight geometry only B1!
dnBy/dxn /B1 x Rnref | 
B0 | 1.50E-02
B1 | 1.00E+00
B2 | -4.60E-03
B3 | -1.11E-03
B4 | 8.52E-03
EB and D. Barna, WG – field quality

## Slide 17: Field Quality for curved magnets 3/3
Open questions:
  What/how to measure field quality?
  How to generate gradients  D. Barna & D. Veres algorithm for CCT winding
  Integrated vs. Fringe field?
  How to qualify magnet / How to model !!!
EB and D. Barna, WG – field quality

## Slide 18: 1) Helium warm synchrotron
M. Vretenar et al., IPAC22
He is interesting in-between protons and C-ions:
  sharper Bragg peak and fall-off to protons,
  but less scattering and nuclear fragmentation compared to carbon.
  Lower neutron dose than protons or carbon.
  Improved RBE to protons, less damaging LET than carbon.
Max 220 MeV/u (30 cm range)
Brho=4.5 Tm
Magnet design
1.65 T dipoles of length 2.65 m and 140 mm x 70 mm aperture.
Water-cooled with 13 A/mm2 current density.
Coil space is compatible for superconducting upgrades for carbon.
Corrector magnets with dipole, quadrupole and sextupole fields.
Pickups in dipoles to save space.
Proven technology, compact & upgradable

## Slide 19: Delivery of 2 Gy in a 1liter tumour: HOW?
Courtesy MedAustron
HIMAC, Iwata et al, NIM-A
TOMORROW(?) … deliver the entire *high intensity* beam in <500 ms for FLASH irradiation
TODAY: Every change of energy  A different cycle
TODAY in Japan: Multi-Energy Extraction (going down or up) within same cycle
Collaboration w. CNAO, MedAustron, HIT, CERN ABT

## Slide 20: Multi-turn injection of 2e10 C-ions
A. Advic, U. Sarajevo (2019)
EB, playing to increase brightness
LEIR injection (S.Maury, C.Carli, D. Mohl)
ECR source ~200 uA C+4
Next generation ECR (e.g. AISHA, Catania) ~600 uA C+4 (in 0.3 mm mrad rms)
Injecting @ 5 MeV/u in a 70 m circumference
Assume 90% (high!) efficiency from source to injection  13 “effective turns” needed (30 for the compact 30m)
~similar #turns for He-ions
(source 1mA)
Collaboration w. INFN, Bevatec, CNAO, MedAustron

## Slide 21: New Linac Design
New injector linac (than the EU facilities) for lower cost, higher intensity
Defined optimal injection energy to the synchrotron
  5 MeV/u for C, He ions
  10 MeV/u for p
Advanced source AISHA (INFN Catania)
Radioisotopes production: feasible with small changes in the baselines
    duty cycle 10%
    staged Linac
RI supported by several communities: HITRIplus, INFN, new EU calls
Within HITRIplus partners and new EU calls

## Slide 22: Slow extraction on the 3rd order resonance
https://indico.cern.ch/event/1076027/timetable/#20211006
Courtesy Rebecca Taylor
Simulations for benchmark with PIMMS (CNAO, MedAustron)
Obtained using pyNAFF!
Spill Quality
Collaboration w. CERN ABT, CNAO, MedAustron, HIT
Go to slideshow for the animation

## Slide 23: Slow extraction on the 3rd order resonance
https://indico.cern.ch/event/1076027/timetable/#20211006
Courtesy Rebecca Taylor
Simulations for benchmark with PIMMS (CNAO, MedAustron)
Obtained using pyNAFF!
Spill Quality
Collaboration w. CERN ABT, CNAO, MedAustron, HIT

## Slide 24: SC-magnet gantry development
  Gantries for Carbon ions are huge and heavy. Only one SC gantry in operation at NIRS, some studies in Europe.
  Objective: Develop a superconducting gantry with weight lower than 100 tons and length below 16 metres.
  Subject: a «SIGRUM» type gantry, as selected by an expert committee in Dec. 2020.
“U. Amaldi, et. al, TERA and CERN,
CERN-ACC-NOTE-2021-0014 ; NIMMS-Note-002
Supported by different collaboration schemes, HITRIplus, iFAST, INFN,…
M. Pullia, HITRIplus

## Slide 25: Other studies…
Beam dynamics
  Preliminary analysis of acceleration
  Beam stability
  Space charge (very small for Carbon, important for protons, reasonable for Helium)
  Intra-beam scattering
  Collimation/ machine protection
Operation
  Reliable, reproducible, easy-to-operate, easy-to-maintain, medical device
  Fast & safe switching between lines and settings (hardware & controls)

## Slide 26: Summary
NIMMS started 20y after “PIMMS” (which gave birth to CNAO and MedAustron), to enable a next generation of medical facilities.
A toolbox of CERN core technologies and competencies, with impact on society - medicine: Superconducting magnets, Mechanics, Linac, Beam dynamics and AI/ML
Users are existing medical facilities and potential new centers, such as SEEIIST, in the South-East Europe
Rich program profiting of collaborations!

## Slide 27: Questions?
elena.benedetto@cern.ch