## Slide 2: Ion production space charge
Ions experience the electric field due to their neighbours – space charge – and repel each other.
Effect is worst when ions have low energy – faster acceleration = better beam.
Conventional ion sources extract ions with energies of a few 10’s of keV and accelerate that beam over several metres.
Laser-target system accelerates ions to MeV energies over distance of 100’s of mm – space charge effect is much reduced.
Duoplasmatron – source Evan Mason 7/7/16

## Slide 3: 4 Objectives Simulation Scapa Diagnostics Tests High rate tests

## Slide 4
SCAPA
Cerberus
Zhi

## Slide 5
Experiments & Technology Development in 2-year Programme: Characterising Source and Benchmarking Simulations
J.S Green et al., NJP. 12 (2010) 085012
R. Prasad et al., Nucl. Instrum. Methods. 623.2 (2010): 712-715.
Established Diagnostics…
Established Targetry…moving toward Hz-level targetry
Typical 9-target array
Tape targetry system (online in SCAPA 2022)
….to build a systematic parameter space map of the source performance
Energy, Flux, Divergence across multiple ion species
..but also need to consider some other experimental contributions like temporal contrast

## Slide 6
Experiments & Technology Development in 3-year Programme: Producing a stable, high-rep source
D. Marsical et al. , Plasma Phys. Control. Fusion 63 (2021) 114003
Courtesy of C. Palmer
Novel Liquid Targetry
ML/AI Control & Optimisation
Implementation of advanced (existing) particle diagnostics, taking account of long term operation.
Implementation of full laser diagnostic suite to support automation, stabilisation.
Reduces production of debris
Increases operational time and possible rep rate
Advanced Particle & Laser Diagnostics
Application of ML techniques (e.g Bayesian Optimisation) for parameter space
Application of AI techniques (DNNs, CNNs) for system control and virtual diagnostics

## Slide 8: WP3 - Proton and Ion Capture Gabor lens
doi: 10.1038/160089b0
doi: 10.3389/fphy.2020.567738
Plasma
Er
Notes: Little Gabor detail to be given.
Non-neutral plasma confined by electric and magnetic fields.
Non-neutral plasma generates radial electric field, which focuses ion beam.
Focal length a function of plasma parameters (& ion beam)

## Slide 9: Stability Density
Objectives.
Initial experiments – establish stable high ‘fill factor’ plasmas
Phase 2. New apparatus to access higher densities - Tests at SCAPA

## Slide 10: Plasma in ALPHA for production
E-field & large radius deleterious
  Low density
  Small radius
Experimental diagnosis
  MCP imaging
  Mode analysis
Modelling
Manipulation techniques
  Cooling (evaporative)
  Rotating wall
  Feedback/damping
doi: 10.1103/PhysRevLett.120.025001 doi: 10.1016/j.nima.2003.09.052
doi: 10.1063/1.4801067 doi: 10.1103/PhysRevLett.106.145001
doi: 10.1103/PhysRevLett.100.203401
Notes: ALPHA want’s near axis particles/plasma with low fields/energies.
Opposite to Gabor lens but control & understanding is is critical to achieving success
Heavily diagnosed experiment with powerful e.g. MCP imaging & modes analysis of trapped plasma
Experimental diagnosis backed up with theory & computational modelling
These diagnosis have enabled manipulation techniques to be implemented – such as RW (see plasma density increases) & SDREVC (notice reproducibility of plasma)
Significantly improving study of systematics & subsequent improvements

## Slide 11
Rw = 2.86cm
(Rp/Rw < 0.2)
1014 – 1015 m-3
Notes: Lower densities (10^14 m^-3), and <20% fill factors, but stored for ‘weeks’. Tesla level fields. 5-20cm length.

## Slide 12: Year 5 milestone
Current
Year 2
Year 5
Final
Notes: End of 5th year milestone is to have studied plasma that have focal lengths of a few metres, comparable to many of the lens elements.
Know which 1-2 parameters need to be improved by x2 to reach final ~1m focal length lens. This is opposed to the decades improvement of many parameters needed to reach here.

## Slide 14
Ion Acoustic Dose Mapping
Is it possible to get the deposited dose using acoustic measurements ?
Compatibility with medical ultrasound and possibility of use in vivo

## Slide 15: Ion Acoustic imaging
Time reversal
Model based minimisation
Back projection

## Slide 16
The SmartPhantom
Aim is to compare measurements:
proton acoustic
scintillating fibre
dosimetry
Compare measurements & simulations:
protons in water (GEANT4)
protons in detectors (GEANT4)
acoustic signals (k-Wave)
Water-filled phantom useful for protons, few 10s of MeV up
www.ptwdosimetry.com
Beam is measured using scintillating fibre planes
Scintillating fibre -> clear fibre -> detector
Aiming to use the edge of the plane as a connector
Clear fibres bundled and sent to CMOS camera
For faster readout, could use photodiodes
From: Medical Applications for Particle Physics (PhD Thesis), H.T.Lau, Imperial College (2021)
Methods of joining fibres – Jeff Sykora, ISIS
http://www.k-wave.org/
https://geant4.web.cern.ch/
SmartPhantom is a tool go on the endstations, to compare simulations of beam interactions with experiment

## Slide 18: WP5 – End station development & Instrumentation

## Slide 19
User engagement – Peer group consultation.
Automated Handling
Controlled atmosphere
Acoustic Imaging
Cellular imaging
In-vivo irradiation
MC40 cyclotron operation for testing and de-risking.
Beamline instrumentation
Gas jet beam profiler.
Dosimetry verification

## Slide 21: WP6 – Facility design and integration

## Slide 23: Facility – planning - development
Ion therapy Research Facility ITRF
£2M budget, of which
£1.5M LhARA – as presented
£500k Facility Engineering plus alternative technologies. 3.35FTE: Mechanical, Electrical, Controls, Tech Services, Vacuum, Radiation Protection

## Slide 25: Top Level Risks

## Slide 26: LhARA - Project organisation
WP1 – Project management
WP2 – Laser Driven proton and ion source
WP3 – Proton and Ion Capture
WP4 – Real-time dose-deposition profiling
WP5 – End station development & Instrumentation
WP6 – Facility design and integration

## Slide 27: Project management
All the boring but essential planning and organisation, but also..
Engagement and outreach:
Stakeholder
Peer group
User community
Public
Patient
Diversification of LhARA funding

## Slide 28: Work Package Managers : Expectations
Progress meetings ever 2 weeks, plus any extra required – minuted on Wiki
Monthly update to LhARA PM – to STFC PRC
  Simple format – fill the blanks.
Milestones
Collaboration Meetings
Deliverables.

## Slide 29: LhARA Wiki

## Slide 30: Documentation
Level1-level2-level3-level4-number-version-description.document type
ITRF – pa1 – wp1.1 – rpt – 0002 – v0.3 – LhARA document naming convention.docx
Documents generated by the LhARA collaboration that are to be stored in the ITRF documentation store must be converted to .pdf format. The copy on the ITRF server must be treated as a read only pdf copy that must not be modified to avoid multiple copies of the same document, protecting version control.
When a document is to be transferred to ITRF it will be given a second ITRF document name which will be recorded above its original LhARA name. This second name must be recorded in the original LhARA document to link the two documents.

## Slide 31: Deliverables
D1. Early review of progress towards CDR.
D2. Interim review of progress towards CDR.
D3. Early draft of LhARA CDR.
D4. Complete LhARA CDR.
Milestones
A total of 16 spread across 5 work packages – all reviewed at Collaboration meetings and all feeding into above Deliverables.

## Slide 32: LhARA Review
1st session – 30th August 2022
2nd, 3rd sessions 29th and 30th September
https://ccap.hep.ph.ic.ac.uk/trac/wiki/Research/DesignStudy/Reviews/AugSep22/Review