## Slide 2
Solenoid requirements
Equivalent field of a solenoid
1st solenoid most demanding
  Choose nominal design with 1 m long coil (Gabor lens flange-to-flange space is 1.157 m)
Solenoids 2 to 5
  Different design (for lower material cost, power consumption)

## Slide 3
Choice of material
Normal conducting
Superconducting
Very high current density compared to conventional conductors
Negligible power consumption
Complicated structure: rigid coil former + insulating cryostat (large space requirement around the coil)
The cryostat/cooling infrastructure needs careful maintenance
Cost of superconducting coils is significantly higher than the cost of conventional conductor
(Hollow copper conductor)
Very common design in many accelerator magnets
Efficient cooling
  water in direct contact with the source of heat
Coils potted in resin are typically very robust
Each cable has to be insulated
  adds complexity and requires more space
Weight of the coils is typically high
Cooling and electric circuits are interwoven, but need separation at the their ends
  pressure drop leads to complex cooling circuits for large coils + increased risk of water leakages
Aim of this design exercise: evaluate the requirements and performance of a normal-conducting solenoid that is suitable for LhARA

## Slide 4
SC solenoid for LhARA
Preliminary design and analysis (A. Beqiri)
Nb-Ti
2-stage cryo-cooler (45 W)
Coil: 1 m, 1.3 T, 250 A, 2 layers

## Slide 5
SC solenoid for LhARA
2-D magnetic and thermal model

## Slide 6
NC Solenoid–param. space

## Slide 7
NC Solenoid–Graded coil design
Use more than one transverse size for the copper cable
Increase the diameter of the cooling channel in the layers further away from the bore
  by keeping the conducting area constant
2 layers, cable size C
2 layers, cable size B
2 layers, cable size A
A
B
C

## Slide 8
400 A NC Solenoid
26 total layers
Graded coil
  3 types of cable
Each point is a different configuration with
  layers, cable type A
  layers, cable type B
  layers, cable type C

## Slide 9
NC Solenoid–2D FEMM Models
400 A
1000 A
2000 A
400 A
1000 A
coil
cover
Field on axis

## Slide 10
1000 A NC Solenoid–specifications
T
19 cm thick coil
925 kg
125 kW

## Slide 11
Simulation capabilities
The instability was observed in PIC simulations
Range of plasma lengths and densities limited by CPU time
Analytical model also available
Several critical parameters
  Number of electrons
  Plasma length and radius
  Plasma temperature
Plasma Simulations
(A) Diocotron mode

## Slide 12
Plasma Simulations
(B) Stable electron plasma
Simulation capabilities
Transverse/Longitudinal plasma profile
Can provide field maps for beam tracking
Simulation times limited to 10s of s
Plasma length
Plasma radial profile
Analytical models also available:

## Slide 13
Plasma Simulations
(C) Instabilities

## Slide 14
http://dx.doi.org/10.23732/CYRCP-2020-007.143
Aim: focus high intensity ion beams–improve focusing quality and reduce the emittance growth
(+ space-charge compensation)
GL tested so far:
>20 years of investigations in Frankfurt
“The formation of an electron cloud in the GL2000 is expected to take at least longer than in the previously investigated lenses.”
30 kV
50 kV
(rp=5 cm)
6 kV
6.5 kV
<30 keV Ar-, He- beams
<130 keV, 35 mA Ar1 beams

## Slide 15
Types of lenses at IAP, Frankfurt
O. Meusel, 2010
K. Schulte, 2006

## Slide 16
Beam transport measurements
1.2 mA, 440 keV, He+ beam
O. Meusel, HIAT2012
Lens filling degree
Beam emittance growth

## Slide 17
Beam transport measurements
He+ beam, emittance dominated transport (test performance of the lens as focusing device)
IPAC2013, THPWO021
GSI, 2012
aberrations

## Slide 18
Pulsed high-field solenoids
< 19.5 T, 2 or 3 pulses/min.
S1, S2: 40 mm bore diameter
14° half-angle geometrical acceptance
Measured transmission (18.6 MeV protons)
  50.6% (dual solenoid)
  28.6% (single solenoid)
Particle loss due to single solenoid
Limited aperture
Spherical aberrations (highly divergent protons travel closer to the windings)
GPT sim.
protons at source (251 MeV)
https://doi.org/10.1038/s41598-020-65775-7

## Slide 19
Active plasma lenses
1 mm-diameter Ar gas-filled capillary, 33 mm length
13 mm behind the tape drive target
transport efficiency through the APL (protons >1.5 MeV)
https://www.nature.com/articles/s41598-022-05181-3
APL
DOI: 10.1103/PhysRevLett.115.184802