## Slide 1: Some studies with linear optics tool …

## Slide 2: Linear optics “calculator”
Last contribution to WP6 Jul23 (!, time flies)
Since then:
  Implemented basic b/l elements:
    Including cylindrical cavity and Gabor lens
  Scripts for DRACO, LION, LhARA Stage 1, (BioPoP old iteration)
Now:
  Have first implementation of Maria’s WP2-blessed TNSA source spectrum for protons
  Integrating visualisation tool coded by students
Value?
  My education!
  Checks, quick calculations
  Engagement with (e.g.) u/g and p/g project students

## Slide 3: Comments:
For LhARA, only energy selection collimator implemented
Cavities implemented as low-field, 200 MHz, cylindrical cavities:
  Almost no effect w\ present configuration
Gabor lenses implemented using solenoid paramters:
  i.e. same i/p for Gabor lens, code calculates, e.g., electron density to give equivalent focusing strength
2x106 protons generated at source “towards” nozel
  I.e. cut on cosq at generation
Beam pipe radius:
  0.5 m (too large)
  0.035 m (too small?)

## Slide 4: Source
Laser-driven TNSA (MM)
Energy distribution from ?? (ref from MM)
Angular distribution flat in cosq and f
Gaussian
Mean 15 MeV, width 2%
Angular distribution flat in cosq and f

## Slide 5: Source
Laser-driven TNSA (MM)
Energy distribution from ?? (ref from MM)
Angular distribution flat in cosq and f
Gaussian
Mean 15 MeV, width 2%
Angular distribution flat in cosq and f
Comparison at end of Stage 1 lattice; solenoid focusing; beam-pipe radius 0.5 m

## Slide 6: Source
Laser-driven TNSA (MM)
Energy distribution from ?? (ref from MM)
Angular distribution flat in cosq and f
Gaussian
Mean 15 MeV, width 2%
Angular distribution flat in cosq and f
Comparison at end of Stage 1 lattice; solenoid focusing; beam-pipe radius 0.035 m

## Slide 7: Focusing: TNSA source
Solenoids
Gabor lenses
Comparison at end of Stage 1 lattice; beam-pipe radius 0.5 m

## Slide 8: Focusing: TNSA source
Solenoids
Gabor lenses
Comparison at end of Stage 1 lattice; beam-pipe radius 0.035 m

## Slide 9: Focusing: Gaussian source
Solenoids
Gabor lenses
Comparison at end of Stage 1 lattice; beam-pipe radius 0.5 m

## Slide 10: Focusing: Gaussian source
Solenoids
Gabor lenses
Comparison at end of Stage 1 lattice; beam-pipe radius 0.035 m

## Slide 11: Energy-selection collimator
Before
After
Comparison at end of Stage 1 lattice; solenoid focusing; TNSA source, beam-pipe radius 0.5 m

## Slide 12: Energy-selection collimator
Before
After
Comparison at end of Stage 1 lattice; solenoid focusing; TNSA source, beam-pipe radius 0.035 m

## Slide 13: Energy-selection collimator
Before
After
Comparison at end of Stage 1 lattice; Gabor lens focusing; TNSA source, beam-pipe radius 0.5 m

## Slide 14: Energy-selection collimator
Before
After
Comparison at end of Stage 1 lattice; Gabor lens focusing; TNSA source, beam-pipe radius 0.035 m

## Slide 15: Longitudinal phase space
Solenoids
Gabor lenses
Comparison at end of Stage 1 lattice; beam-pipe radius 0.5 m

## Slide 16: Longitudinal phase space
Solenoids
Gabor lenses
Comparison at end of Stage 1 lattice; beam-pipe radius 0.5 m

## Slide 17: Conclusions
Continue development, search for bugs!
Preliminary conclusions, or things to (re)evaluate:
  TNSA source gives different distributions to Gaussian:
    Pattern or particle loss, excursions in focusing, …
  Gabor lens focusing not identical to solenoid focusing:
    Either need to tweak strengths, move collimators, (find errors)
  Beam-pipe/stay clear:
    Could just be my problem, but, need to check values
  Study longitudinal phase space and specification of cavities:
    May be able to profit from JAI project results
Need to reset default simulation to use:
  Reference parameterised TNSA source
    M.Maxouti with N.Dover et al; interface proposed to W.Shields
  Gabor lenses:
    Transfer matrix and field map
Electron densities required to get equivalent solenoid need to be reviewed w.r.t. WP3 programme