## Slide 1
WP6 Weekly Meeting
Injection Line Update
William Shields
(william.shields@rhul.ac.uk)
28th January 2025

## Slide 2
Layout & Engineering
New injection line converted to BDSIM
Updated magnet geometry needed from Ta-Jen
  New spiral angle
BDSIM model to be updated from CAD
  Magnet + RF
Angled shielding wall to be added.
Next iteration to add shutter, PMs, vacuum valves, etc.

## Slide 3
Optics Performance
Good MADX & BDSIM model agreement.
GPT model still in development.
Beam at the injection magnet exit:
εx : 4.12e-06
εy : 4.08e-06
⍺x : -0.00082
⍺y : -1.03171
βx : 0.934
βy : 2.129
Dx : -0.400
Dy : -0.003

## Slide 4
Aperture & Collimation
Wide aperture needed (8cm minimizes losses)
  Max beam radius (1σ): 2cm
Collimator envisaged at either:
  S~10.5m - close to FFA magnet
  S~4.5m - close to dipoles