## Slide 1
LhARA
A bio-centered plan
LhARA collaboration meeting 28/07/26 | Recap of PoPLaR discussions

## Slide 2
The long-term vision
A single facility with automated end stations, capable of supporting:
FLASH
Ultra-high dose-rate irradiation
SFRT
Spatially fractionated radiotherapy
Advanced imaging
High-resolution imaging systems
Beam monitoring
Advanced beam monitoring techniques

## Slide 3
SHORT-TERM PROJECT 1
PoPLaR
Radiobiology, adapted for laser-driven beams
Current plans
Improving the setup and efficiency of the radiobiology experiments.
Working out how standard protocols and instrumentation need adapting for laser-driven beams.
Overall aim
Once established, PoPLaR becomes the comparison baseline against x-ray and cyclotron proton beams, via:
Clonogenic Survival Assays
Comet Assays
Fixed Immunofluorescence Imaging

## Slide 4
SHORT-TERM PROJECT 1
PoPLaR
Radiobiology, adapted for laser-driven beams
Expected Beam Differences
We know that our current laser-driven proton beam differs from cyclotron-accelerated proton beams by: divergence, energy spectrum, dose rate, and shot-to-shot variability.
Biological Hypotheses
Due to these differences, we expect the following assays -- at the same average dose, across multiple cell lines (cancerous and normal tissue) -- to show measurable differences:
Clonogenic Survival Assays
Comet Assays
Fixed IF Staining & Imaging
CYCLOTRON
Consistent survival curve; shoulder and slope match predicted RBE~1
LASER-DRIVEN
Potentially higher survival at same nominal dose at ultra-high dose rates (FLASH sparing)
More variation- mixed LET spectrum gives mixed RBE
CYCLOTRON
Uniform tail moment across cells; damage matches simple-DSB model
LASER-DRIVEN
Wider spread of tail moments to reflect the variation of dose delivery across the cell dish, as well as across replicates due to shot-to-shot variation
CYCLOTRON
Evenly distributed foci per nucleus; foci scale linearly with dose
LASER-DRIVEN
Foci counts vary more across the field and between replicates, also may see a reduction of foci at ultra-high dose rates
The aim of these experiments are to, with instrumentation and better beam characterisation & monitoring, reduce some of the variations and get a more comparable biological outcome in the 3 experiments.

## Slide 5
SHORT-TERM PROJECT 2
Live-cell imaging
Watching damage and repair as it happens
Plan
Building a custom live-cell imaging system to compare damage and repair in real time, across different particle therapy modes and acceleration methods.
What it feeds into
Tony's SFRT work
Provides direct support for the spatially-fractionated radiotherapy programme.
FLASH comparisons
Gives us a ready tool for comparing ultra-high dose-rate effects too.
Overall aim
2nd line of comparison for laser driven beams, look at underlying mechanisms.
Hypotheses pending, depending on fixed results.