## Slide 1
‘
X THE PLACE OF USEFUL LEARNING
PoPLaR In-Person Meeting
Birmingham University
Summary, analysis and outlook of PoPLaR/LhARA experiments within SCAPA…and beyond
24th February 2026
Dr. Robbie Wilson
robbie.wilson@strath.ac.uk

## Slide 2
Parameters | 
Peak Power | 350 TW
FWHM pulse duration | 25 fs
Energy per pulse (on target) | 7 J
Pulse repetition rate | 1 Hz
Temporal intensity contrast | 1010:1 @ 100 ps 108:1 @ 30 ps 104:1 @ 2 ps ASE contrast 1010:1
Central wavelength | 800 nm
Beam quality Strehl ratio | 0.85
Parameters | 
Peak Power | 
FWHM pulse duration | 
Energy per pulse (on target) | 
Pulse repetition rate | 1 Hz
Temporal intensity contrast | 1010:1 @ 100 ps 108:1 @ 30 ps 104:1 @ 2 ps ASE contrast 1010:1
Central wavelength | 800 nm
Beam quality Strehl ratio | 
SCAPA: Scottish Centre for the Application of Plasma-based Accelerators
Research is focused on the development and application of laser-driven particle acceleration.
Can deliver high particle numbers (>108 protons), within the MeV energy range, at Hz level repetition rate.

## Slide 3
Mechanism for laser-driven ion acceleration
Target Normal Sheath Acceleration (TNSA)
Proton beam characteristics
Laser energy absorbed producing large population of hot electrons
Generates strong (TV/m) electrostatic sheath fields at target rear
Drives acceleration of high energy (MeV) protons
Hot electrons injected and propagate through the target
Broad energy spectrum, up to a maximum cut off energy.
i)
ii)
Proton energy-dependent beam divergence.
0
1
0.5
Ep/Ep Max
0
1
0.5
Ep/Ep Max

## Slide 4
Update on Experiment Stages & Gateways
I. Design & Procurement
II. Assembly & Alignment
III. Source Characterisation:
16th – 28th June
IV. Radiobiology:
27th Oct – 21st Nov
Start of BP1 funding
Order of PMQ XYZ stage (5-7 week delivery)
Order of cell station vacuum parts (4 weeks delivery)
Manufacture of thin window
Manufacture of Oxford cell station
Construction of the cell station
Construction of updated TP beamline
Definition of an offline alignment line
Construction and offline alignment of PMQ setup
Install of PMQ system in vacuum chamber
Change of parabola
1/2 weeks of SCAPA beamtime
Laser Beamline alignment (0.5 days)
Source optimisation w/o PMQ (0.5 days)
PMQ transmission, activation and debris test (0.5 days)
Lanex/beam profiler measurement at end of beamline (1 day)
PMQ position optimisation (0.5 days)
RCF measurements through beamline (0.5 days)
Full cell assembly RCF measurement (0.5 days)
3 weeks of SCAPA beamtime (with potential for a gap between the alignment week)
Laser Beamline alignment (0.5 days)
Source optimisation with PMQs (1 day)
Dosimetry and source stability measurements (2 days)
Cell irradiation (6.5 days) + regular dosimetry

## Slide 5
SCAPA Bunker B Target Station

## Slide 6
Proton Capture Beamline
Internals
Currently have a x2 PMQ system;
Target to PMQ1 front: 80 mm
PQM 1 to 2: 132 mm
Each xyz and rotation on each
Can add proton beam scatterers to improve the proton focus spatial-profile. Tested various materials and thicknesses.
Currently cannot operate our ion spectrometer without removing and realignment of PMQs.
Proton focus – With Scattering foil
Proton focus – Without Scattering foil

## Slide 7
Proton Capture Beamline
Externals
50 µm thick Mylar window for proton exit.
Air gap length: 128 mm (can expand to 190 mm).
We have variable path vacuum pumping and gate valves to enable rapid switching of modes.
In vacuum insertors for extra diagnostics or filtering.
i) TP-Vacuum Mode
iii) Proton Focus Imager (Lanex)
ii) RCF Stack
iv) Cell Irradiation Mode
4 Operation Modes (currently)

## Slide 8
Source Updates
Experiment 1– June 2026
Measured= (12 ± 2) MeV using the Thomson Parabola (TP) Ion Spectrometer.
is relatively stable. However, did not do a longer scan (>100 shots) to see other sources of degradation (as we switched to PQM setup).
Note can drop to 10 MeV if the focal spot not optimised (demonstrates the sensitivity of alignment).
RCF stack close to the target rear before the focal spot was optimised, to confirm and beam divergence.
Can now retrieve real proton numbers from our TP. A calibration was made with comparable RCF stack and TP spectra over several shots.

## Slide 9
Source Updates
Experiment 2– October 2026
We measured increased = (14.4 ± 1.2) MeV using the Thomson Parabola (TP) Ion Spectrometer.
This increase is in part due to higher pulse intensity, but this does not fully explain the result.
Made RCF measurements comparing the beam generated for two target materials; Steel and Kapton.
Steel provides a cleaner proton beam but opens us up to EMP issues.
Steel
Kapton

## Slide 10
Identified Issues, potential solutions and areas to improve
Cell irradiation timescale
Source beamline diagnostic
Proton capture beamline
Proton dose diagnostics
Proton source
stability

## Slide 11
Irradiation Time and Routes to Improvement
Shot Rate Oct/Nov beamtime: 1 shot every 20 seconds
Most shots in one cycle was 50 (4,7,14 x2) so 1000 seconds = 16 mins 40 seconds.
This does not include transport time, time between runs (to rotate carousel), mounting time, lock up/prep time and post irradiation radiation checks…so more like 30-40 mins.
Aim for 1 shot every 5 seconds (could push to 1 Hz/1 second in future).
50 shots (4,7,14 x2) can be done in 250 seconds = 4 minutes 10 seconds.
Split cell irradiations from RCF irradiations or remove RCF shots for a new on-shot diagnostic with cells (RCF before cell dish?).
Spilt cell irradiation runs. Would take longer overall, but much shorter in/out time.
Timescales November beamtime
Timescale Improvements
Characterise proton focus with Lanex Imager /RCF stack
Open area and add cell carousel and RCF (rotation and alignment checks)
Lock up area and checklist
Irradiation runs and RCF shots
Open area and radiation check

## Slide 12
Proton source stability- Known Issues
Over a series of shots, we measure a decrease in approx. 1 MeV over 120 shots.
A result of reduced laser energy on target due to pellicle damage (the optical film protecting the focusing optic from debris).
This occurs due to debris build up and asymmetry/structure in the laser near-field spatial-intensity profile.
Key to PoPLaR- We do not measure TNSA proton spectrum on every shot, so must rely on secondary correlated diagnostics.

## Slide 13
Proton source stability- Unknown Issues
Measured a large variation in proton focus dose using the RCF (more details on next slide).
This is also seen using the diagnostics to measure the degree of laser light reflected from the target (both in backscatter and specular direction)

## Slide 14
Proton source stability- Proton Imager Issue
Three key points of note from this;
Proton focus – With Scattering foil
Proton focus – Without Scattering foil
Lanex scintillator, filtered for 8 MeV proton (7 layer of Mylar)
TNSA spectrum
Energy (MeV)
Signal
Lanex
Ep,max
Footprint Signal
Signal
Ep,max
Footprint Signal
or
or equal
PMQ focus spectrum
Lanex
8 MeV
Energy (MeV)
i) Not having the ability to switch back to TP is a key issue to highlight.
ii) Relying on proton focus imager can be misleading due to narrow energy window. Require spectrum reconstruction.
iii) The need for on-shot primary or secondary diagnostics, that can map the full spectrum.
8 MeV

## Slide 15
C. J. McQueen et al., Communications Physics 8, 66 (2025)
Synthetic diagnostic of proton spectrum

## Slide 16
Capture Beamline
Identified Issues
Potential Solutions/Improvements
Proton focus- Low dose (with scatterer).
Better monitoring solutions of PMQ positions and improved diagnostics.
Proton focus- High degree of spatial structure (without scatterer).
Hysteresis on some drives, limiting accurate replacement of PMQs.
Distance to target limited, which influences proton capture.
No transverse movement to remove PMQs from TP line.
Upgrade to x4 PMQ system
(would require significant engineering to add/modify setup).
Modifications to mounting of PMQ1 and target.
Add larger stages to each PMQ to move out of beam central axis.
Upgrade to x4 PMQ system
(would require significant engineering to add/modify setup).

## Slide 17
Future Beamtime in SCAPA and Beyond
SCAPA
Cell Studies
Proton Capture system
Diagnostic Development
Repeat Nov 2026 beamtime with improved cell irradiation durations/lessons learnt.
Test the influence of irradiation rate, through variation of shot rate to achieve the same overall dose.
Greater knowledge on input source parameters and stability.
Implementation of a > 4 PMQ capture system.
Alter PMQ relative positions to optimised lower Ep capture, potential more stable
Alteration to PMQ movement to enable TP use on demand.
Reduce proton numbers to do fractionated dose irradiation shots.
Energy selector /monochromator to reduce proton focus to one energy.
Improvements to the proton focus imager to enable spectral measurements
On-shot dose measurement, either active or passive (RCF).
Synthetic diagnostic development to predict on-shot TNSA spectrum/divergence.

## Slide 18
Future Beamtime in SCAPA and Beyond
ELI Beamlines – Target Area E4
ELIMED (ELI-Beamlines MEDical and multidisciplinary applications)
ELIMAIA (Multidisciplinary Applications of laser-Ion Acceleration)
https://www.frontiersin.org/journals/physics/articles/10.3389/fphy.2020.564907/full
x5 PMQ beamline and energy selection system.
Built in proton focus dose diagnostics: a Secondary Electron Monitoring (SEM), a Multi-Gaps Ionization Chamber (MGIC), and a Faraday Cup (FC) for absolute dosimetry.
We have worked on this system, with the aim of developing a syntenic diagnostic of the TNSA driven proton beam.

## Slide 19
Future Beamtime in SCAPA and Beyond
Workshop Topics:
Medical applications of laser-driven ion beams (ultrahigh dose-rate clinical dosimetry, radiation therapy, medical radioisotopes, medical imaging);
Ultrafast Radiation Biology (in vivo and in-vitro)
Recent development of compact laser-plasma ion accelerators for multidisciplinary applications.
Radiation damage on electronics and space radiation applications with laser-driven ion beams
Non-destructive material inspections for cultural heritage applications.
https://indico.eli-laser.eu/event/229/

## Slide 20
X THE PLACE OF USEFUL LEARNING
Thank you for your attention